## Slide 1: Incremental problem definition: [P1] Basic Avoidance
Known world - consisting from Free, Occupied, Unknown sets.
Mission - Assumptions 1-5 are valid.
Sensors - LiDAR sensor is introduced as source of information.
Sensor fusion - classification function implementation
Hard Flight constraints - UAS dynamic only.
Problems addressed:
Navigation Loop Implementation (sec. 6.6.2).
Avoidance Loop Implementation (sec. 6.6.1).

## Slide 2: Incremental problem definition: [P2] Intruders Introduction
Sensors - ADS-B added enabling intruder detection.
Sensor fusion - union of obstacle space and individual intruder spaces.
Hard constraints - intruder corridors, changing over time.
Problems addressed:
Intruder Intersection Models (minimal operation requirements achieved): Linear Intersection Model (app. C.1), Body-volume intersection (app. C.2), Maneuverability uncertainty intersection (app. C.3).
Flight Corridors (sec. 6.5.3).

## Slide 3: Incremental problem definition: [P3] Static restrictions
Known world - added restricted space portion evolving over time
Information sources - added Obstacle Map (fig. 6.13), Visibility Rating Concept (fig. 6.12) and Static Constraints (sec. 6.5.3).
Data fusion - the rating implementation of the data fusion (sec. 6.5.4).
Hard constraints - added obstacles and terrain constraints.
Soft constraints - added airspace restrictions and geo-fencing/

## Slide 4: Incremental problem definition: [P4] Dynamic restrictions
Information sources - the weather adding moving constraints (def. 20) example Weather Avoidance Case (app. E.1).
Hard constraints - protection zones against severe weather conditions
Soft constraints - protection zones against mild weather conditions

## Slide 5: Incremental problem definition: [P5] Rules of the air
Soft flight constraints - different behavior in airspace classes added, rules of the air implementation added, introduction in UTM Implementation (sec. 6.7), Rule Engine for UAS (sec. 6.8.1) and Rule Implementation (sec. 6.8.2).